## Slide 1: Multi-level logic Synthesis Dr. Chandan Karfa CSE IIT Guwahati

## Slide 2: Text Book
Chapter 6, Z. Kohavi and N. Jha, Switching and Finite Automata Theory, 3rd Ed., Cambridge University Press, 2010.

## Slide 3: Objective
Introduction to Multilevel logic synthesis
Technology-independent synthesis
  Factoring
  Decomposition
  Extraction
  Substitution
  Elimination

## Slide 4: Two-level vs Multi-level Logic
Multi-level logic realization contains more than two levels of logic gates.
Circuits in which an arbitrary number of gates may lie on any path between a primary input and a primary output.

## Slide 5
xyz + wxz + yz

## Slide 6: Need for Multi-level Logic Synthesis
In some cases SoP representation is impractical
  Example: Parity bit generator, multiplication
Exponential number of implicants in SoP form for parity bit generator

## Slide 7: Need for Multi-level Logic Synthesis
Advantage:
  Multi-level logic circuits require less area and delay compared to the corresponding two-level realizations and hence are more practical.
Disadvantage:
  It is difficult to obtain provably optimal multi-level realizations because of the much larger design space available for exploration.
Phases Of Multi-level Logic Synthesis
  Technology Independent Synthesis
  Technology Dependent Synthesis

## Slide 8: Objectives
Reduces the number of literal in expression
  No of transistors is twice of no of literals
Identifying common sub-expression within an Boolean Expression (for single output) or between multiple Boolean expressions (for multiple outputs)

## Slide 9: Representation
As Logic Network

## Slide 10: Logic Network
input variables (a, b, c, d, e)
primary output variables (w, x , y, z).

## Slide 11: Technology Independent Synthesis
We design the circuit without keeping in mind we have to map that circuit to certain technology.
The problem is intractable.
  Primarily the heuristic based approaches are used.
Technology-independent multi-level logic synthesis is carried out with the help of various logic transformations.

## Slide 12: FPGA Technology Mapping

## Slide 13: FPGA Components

## Slide 14: Interconnections

## Slide 15: FPGA Technology Mapping
Technology Mapping:
ASIC – Cell Library (e.g., NAND, NOT, FF)
FPGA – fixed architecture
  LUT
  DSP
  RAM/ROM
In FPGA:
  Gate level design  LUTs
  Multiplier/MAC  DSP
  Memory/Large Registers  RAM/ROM

## Slide 16: LUT Mapping
Look Up Table
2k SRAM bits
A k-LUT can implement any Boolean function having k-variable,
B: 2k  {0,1}
F = ab + a’b’
a | b | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
2 inputs LUTs

## Slide 17: LUT Mapping

## Slide 18: Introduction to logic transformations
There are various methods of logic transformations. The methods are as follows:
  Factoring
  Decomposition
  Extraction
  Substitution
  Elimination.

## Slide 19: Factoring
A factored form is a recursive sum-of products representation in which the products themselves can consist of a sum of products
In factoring, an expression in sum-of-products form is converted into an expression with multiple levels without introducing any sub-functions.

## Slide 20: Factoring cont'd...
The above expressions can be represented by logic network graphs
the multi-level circuit has six levels of logic.

## Slide 21: Factoring cont'd...
Factoring makes expression more compact.
The minimal sum-of-products expression has 16 literals whereas its factored form has only 11 literals.
The number of transistors in the complex CMOS-gate implementation of an expression is twice its literal-count.
As the number of literal in the expression increases, the implementation complexity of the expression also get increases.
Literal count is good measure of implementation complexity.

## Slide 22: Decomposition
In decomposition, a factored switching expression is replaced with a set of new expressions.

## Slide 23: Decomposition cont'd...
Decomposition replaces subexpression in the expression by set of functions. These functions are said to be implemented separately.
The literal-count after the decomposition is the sum of the literal-counts for each function. Thus, the literal count is now 15.

## Slide 24: Extraction
Extraction is the process of extracting common sub-expressions (CSE) from two or more expressions in factored form.
If there is CSE between two or more expressions, then we replace CSE by a new function.

## Slide 25: Extraction Cont'd...
The literal count reduces from 10 to 9.

## Slide 26: Substitution
Substitution is the process of replacing a subexpression in an expression f with a variable g corresponding to a node in a network graph. In other words, g is substituted into for f is expressed in terms of g.

## Slide 27: Elimination
Elimination removes internal nodes from the network graph.
It becomes possible if the corresponding expression replaces the variable corresponding to that node. Whenever the elimination step reduces the literal-count, it may be useful to employ it.
Example: Consider f1 = x + f2 and f2 = y + z. If f2 is not needed else-where in the network then it can be eliminated in the expression for f1 by replacing it with y + z, thus obtaining f1 = x + y + z. This reduces the literal-count from four to three.

## Slide 28: Approach
In multi-level logic synthesis, the above five logic transformations are applied to an initial logic network iteratively until no more improvement is possible in the targeted objective
  They need not be applied in the given order
Synthesis objectives are optimization of area, delay, or power.

## Slide 29: Example

## Slide 32
Thank You